## Slide 1
SAR Tomography
Basics, Concepts & Techniques
Nesrin Salepci
Friedrich-Schiller-University Jena
Department for Earth Observation
Jena, Germany
Marivi Tello Alonso, Victor Cazcarra Bes
German Aerospace Center (DLR)
Microwaves and Radar Institute (HR)
Oberpfaffenhofen, Germany

## Slide 2: Outline
Mathematical Formulation of Tomographic SAR imaging
TomoSAR imaging geometry & data stack, TomoSAR estimations: reflectivity profiles, tomographic cube & slices, TomoSAR aspects: tomographic aperture, coordinate system & 3D resolution cell
tomographic aperture, system bandwidth, sensor wavelength, scattering mechanisms, polarization, weather & season
TomoSAR imaging model, linear system equation, reconstruction of the reflectivity profiles (inversion), constraints & factors to consider for the inversion, inversion algorithms
Polarimetric SAR Tomography, Differential SAR Tomography
Forest, Urban, Ice & Snow, Agriculture Imaging
Introduction
SAR Tomography Basics
Factors Affecting Tomographic SAR imaging
Advanced Techniques
Case Studies
References & Further Reading
the aperture synthesis in azimuth (SAR), forming baseline (SAR Interferometry), the aperture synthesis in elevation (TomoSAR)

## Slide 3
Introduction

## Slide 4: Synthetic Aperture Radar: the aperture synthesis in azimuth
synthetic aperture
in azimuth
θl : look angle
swath
azimuth
ground
range
flight
path
far
range
near range
θl
range
Aaz
Let’s remember what SAR stands for:
Synthetic Aperture Radar
The key factor that is utilized in SAR is to synthesize a much longer antenna in azimuth direction by making use of the motion of the SAR sensor in order to achieve finer resolution.
SAR imaging geometry

## Slide 5: SAR Interferometry: forming baseline
r1
r2
Δr
B
Bp
θl
reference datum
topography
SAR Interferometry (InSAR) makes use of the phase difference between two complex valued images from different view angle, i.e. forming baseline, so that topography of the area can be imaged.
B : baseline
Bp : perpendicular baseline
θl : look angle
r1 & r2: range distance for the respective acquisitions
Δr : range difference
SAR interferometry imaging geometry
The limitations of InSAR:
It can not separate the contribution of multiple targets from the same range resolution cell,
The reconstruction of a DEM for the areas with steep slopes, e.g. building facades, can fail due to layover.
To overcome such limitations:
SAR techniques using multiple acquisitions, which involve variations of the view angle (multi-baselines) were developed.
Now let’s remember how SAR Interferometry works:
Baseline

## Slide 6: SAR Tomography: the aperture synthesis in elevation with multiple baselines
If more tracks are added to form multi-baselines so that a new aperture in elevation can be synthesized, higher resolution in elevation can be achieved (similar to the aperture synthesis in azimuth)
Since SAR signal can penetrate through canopy, soil, snow and ice, TomoSAR allows for the estimation of volumetric properties, e.g. biomass, ice thickness…
SAR tomography imaging geometry
The principle of aperture synthesis in elevation (3D imaging) is called:
SAR Tomography (TomoSAR)
which uses both phase and amplitude information to locate the backscattering positions in elevation.
synthetic aperture
in elevation
azimuth
ground
range
master track
track 1
track n-1
track n

## Slide 7
SAR Tomography Basics

## Slide 8: SAR Tomography imaging geometry & data stack
stack of
co-registered SLCs
elevation aperture
r0
r1
rn-1
rn
r0 : slant range of the master track
r1…rn : slant range of the slave tracks
θl : look angle
θl
SAR Tomography uses multiple acquisitions from slightly different viewing angles forming an aperture in elevation and locates the scatterers along the elevation which is perpendicular to the radars line of sight.
SAR tomography imaging geometry
The implementation of TomoSAR methods requires:
co-registration of the SLCs with sub-pixel accuracy so that the range-azimuth position corresponds to the same area on the ground
the residual component of the interferometric phase, e.g. atmospheric artifacts, platform motion, must be estimated and subtracted from the phase of the slave SLCs.
scatterers are located on this plane, which is orthogonal to the slant range

## Slide 9: SAR Tomography estimations - reflectivity profiles
TomoSAR algorithms reconstruct for each azimuth-range pixel
the scene’s reflectivity function in elevation.
ground
canopy
Reflectivity profiles of 6 pixels. (The profiles are normalized)
reflectivity profile
along elevation

## Slide 10: SAR Tomography estimations: TomoSAR cube & tomographic slices
azimuth
range
range slice
azimuth slice
In order to visualize the result, usually slices of this data cube are plotted.
azimuth slice: slice parallel to the azimuth dimension
range slice: slice parallel to the range dimension
horizontal slice: slice parallel to the horizontal plane
the color on tomographic slices:
dark blue: min. power, dark red: max. power (phase center)
forest
ground
TomoSAR cube
The reflectivity profiles of every pixel form a TomoSAR cube, whose voxels are defined by the resolution in azimuth, slant & cross-range.
(The slices and the profiles
are normalized for each pixel)
reflectivity profiles

## Slide 11: SAR Tomography aspects: tomographic aperture & coordinate system
TomoSAR coordinate system :
azimuth: flight direction (orthogonal to the page) slant range: radar’s line of sight (with a look angle from nadir) cross range: direction that is orthogonal to the slant range
Tomographic aperture () : the maximum distance between the SAR acquisitions
slant-range
cross-range
azimuth
tomographic aperture
r0
r1
rn-1
rn
Acr : cross range (tomographic) aperture
r0 : slant range of the master track
r1…rn : slant range of the slave tracks
θl : look angle
θl
Acr
slant range
cross range

## Slide 12: SAR resolution cell - resolution in azimuth & slant range
range
azimuth
slant-range
cross-range
azimuth
A SAR pixel = sum of all contributions within the resolution cell
δaz =
Azimuth
resolution
: carrier wavelength
r0 : range distance
Aaz : azimuth aperture
δaz
with the azimuth resolution being a function of the aperture in azimuth
transmitted
pulse
with the slant-range resolution depending on the bandwidth
δsr =
c : speed of light
W : pulse bandwidth
Slant-range
resolution
δsr
[Ferro-Famil, 2015]
SAR resolution cell

## Slide 13: SAR Tomography aspects- resolution in cross range
the resolution cell for single baseline has contribution
both from the canopy and the ground
this tomographic resolution cell has reflectance
only from the canopy
this tomographic resolution cell has reflectance only from ground
SAR resolution cell
Tomographic SAR resolution cell
Acr
With the multiple tracks in elevation the SAR resolution cell is split into multiple layers in cross-range based on the tomographic aperture Acr
δcr =
: carrier wavelength
r0 : range distance
Acr : cross-range (baseline) aperture
Cross-range
resolution
δcr
[Ferro-Famil, 2015]
slant-range
cross-range
azimuth

## Slide 14: 3D resolution cell
δsr =
δcr =
δaz =
= δcr* sin(θl)
slant-range(r)
cross-range (s)
azimuth(x)
θl
δz
δaz
δcr
δsr
Acr
The 3D resolution cell depends on :
Pulse bandwidth along slant range (W)
Synthetic aperture in azimuth ()
Synthetic aperture in cross range ()
Tomographic SAR resolution cell
slant-range
cross-range
azimuth

## Slide 15
Factors Affecting SAR Tomography Imaging

## Slide 16: The effect of tomographic aperture
slant-range
cross-range
azimuth
Acr
slant-range
cross-range
azimuth
Acr
smaller tomographic aperture
lower resolution
larger tomographic aperture
finer resolution
δcr =
Cross range
resolution

## Slide 17: The effect of system bandwidth
reflectivity
ground
canopy
Acr
150 Mhz Bandwidth/7 tracks
slant range resolution is inversely proportional to the system bandwidth!
transmitted pulse
with large bandwidth
cross-range
δsr
[Papathanassiou, 2013]
slant-range
cross-range
azimuth

## Slide 18: The effect of system bandwidth
ground
canopy
reflectivity
elevation
low range resolution can degrade
the ability to resolve the vertical structure!
transmitted pulse
with small bandwidth
δsr
Acr
150 Mhz Bandwidth/7 tracks
6 Mhz Bandwidth/7 tracks
[Papathanassiou, 2013]
slant-range
cross-range
azimuth

## Slide 19: The effect of tomographic aperture & system bandwidth - summary
small tomographic aperture
small bandwidth
large tomographic aperture
small bandwidth
small tomographic aperture
large bandwidth
large tomographic aperture
large bandwidth
resolution in the slant/cross-range plane is a function of:
(tomographic aperture) & (bandwidth)
δsr =
δcr =
slant
range
cross
range
Acr
[Tebaldini, 2012]
slant-range
cross-range
azimuth

## Slide 20: The effect of different sensor wavelength
Since the penetration depth depends on the wavelength of the sensor, the tomographic profiles differ accordingly. For example, in general in a forested area the phase center elevation at L-band is higher than at P-band.
Tomographic profiles of L-band and P-band in HV polarization over a boreal forest. The white arrow indicates the looking angle, and green line is the LIDAR forest height [Tebaldini & Rocca 2012].
X-band
C-band
L-band
P-band
L-band - HV
P-band - HV

## Slide 21: The effect of different scattering mechanisms
transmitted
pulse
backscatter from the canopy
trunk-ground
scattering
canopy-ground scattering
backscatter from the ground
Different scattering mechanisms (SM) result in different reflectivity profiles. For example, forest scenarios can be characterized by : double-bounce, surface and volume scattering mechanisms.
canopy- ground
ground
canopy
trunk- ground
reflectivity
height
trunk-ground: double bounce SM with ground locked phase center (the peak of the reflectivity)
ground & canopy-ground : surface SM with ground locked phase center
canopy: volume SM with phase center located above the ground, depending on the canopy height, and the associated reflectivity curve is spread along the cross-range
[Tebaldini, 2012]

## Slide 22: The effect of different polarization
Tomographic analysis of the three polarization channels with Capon spectra as reported in [Tebaldini, 2012] : HH, HV and VV
HH & VV: characterized by a narrow phase center located mainly at the ground which relates to the scattering mechanisms of double bounce contribution from trunk-ground and canopy-ground interactions
(vegetation is barely visible)
HV : the contribution from the vegetation, relating to the volumetric scattering, is more visible in HV but contribution from ground is still dominant
forest
ground
type of polarization affects the sensitivity to different scattering mechanisms.
[Tebaldini, 2012]
V
H
co-polarization (HH, VV) is more sensitive to the surface scattering and double-bounce, whereas cross-polarization (HV, VH) is more to the volume

## Slide 23: The effect of weather & season
tomographic slices before & after a rainfall
tomographic slices in spring & autumn
LIDAR
LIDAR
LIDAR
LIDAR
3D distribution of the reflectivity is influenced by
after rain:
The ground power is reduced w.r.t the canopy power
The height of the phase center (red areas) is increased
leaf off:
The ground power is increased w.r.t the canopy
weather: due to the dielectric properties of the target
season: leaf-on, leaf-off conditions
According to a case study by [Pardini et al. 2014] over a temperate forest, Traunstein, Germany:
LIDAR

## Slide 24
Mathematical formulations & Inversion Algorithms

## Slide 25: The TomoSAR imaging concept : tomographic stack
P(x, r) : pixel in xth row at azimuth and rth column in range
N : number of tracks (number of acquisitions)
Let‘s assume that our dataset is a stack of N SAR images :
All the slaves are co-registered to a master
The flat-earth phase is compensated at each slave
(as well as the contributions from atmosphere, platform motion etc.)
N
P(x, r)
range
azimuth
Reflectivity information based on elevation is encoded
in the N number of pixels at position (x, r)
yN: measurement vector containing the N number of complex pixel values at location (x,r)
y1
y2
y3
.
.
yN
Nx1
yN =

## Slide 26: The TomoSAR imaging model
θl
s
r
b
reference surface s=0
nth
image
master
bn
The TomoSAR imaging model can be formulated as a simple principle:
a Fourier relation exists between SAR data and the target projection
However with this equation,
proper reconstruction of the vertical profiles of the scene requires uniform distribution of the baselines
the limited number of passes often results in a strongly undersampled observable vector
yn (x, r) =
the complex pixel value from Nth SAR images at the azimuth (x) and range coordinates (r)
SAR reflectivity along the cross-range (s) for pixel (x,r)
the phase of the pixel depends on the normal baseline of the Nth image (bN), carrier wavelength () and range distance (r0)
[Ferro-Famil, 2015]
Hence the reflectivity distribution can be retrieved by performing the Discrete Fourier transform (DFT) of the observable vector (yn) with respect to the normal baseline
=DFT{yn (x, r)}

## Slide 27: The TomoSAR imaging model
θl
s
r
b
reference surface s=0
nth
image
master
bn
To avoid those shortcomings many approaches have been presented in the literature with the fundamental assumption that:
the estimation of the scene reflectivity is traced back to the finding the best spectral estimator of the SAR spectral intensity distribution in a statistical sense
spectral intensity distribution is retrieved by estimating the multibaseline covariance matrix, formed with the interferometric pairs of the measurements by , which requires spatial multilooking
Rn (x, r) =
Covariance between the slave image yn(x,r) and the master image
Spectral intensity distribution
the phase of the pixel depends on the normal baseline of the Nth image (bN), carrier wavelength () and range distance (r0)
The equation for TomoSAR imaging model can be rewritten as:

## Slide 28: The linear system equation
Rn (x, r) =
R = A
R : covariance between slave and master image
A : steering matrix (N*h mapping matrix with Anh = )
: discrete intensity distribution vector with discrete elevation positions sh (1,…..,H)
Discretizing the elevation profile
leads to a linear system equation
TomoSAR imaging model can be approximated by discretizing the intensity distribution
N
h
h : number of discretization
reflectivity profile

## Slide 29: Reconstruction of the reflectivity profile : Inversion
R = A
RN: vector containing the covariances
a: steering vector containing values derived by
=
Nxh
a(r1,4)
a(r2,4)
a(r3,4)
a(r4,4)
.
a(rN,4)
.
A
a(r1,1)
a(r2,1)
a(r3,1)
a(r4,1)
.
a(rN,1)
=
a(r1,2)
a(r2,2)
a(r3,2)
a(r4,2)
.
a(rN,2)
a(r1,h)
a(r2,h)
a(r3,h)
a(r4,h)
.
a(rN,h)
…
…
…
…
…
…
R1
R2
R3
R4
.
RN
Nx1
hx1
R
covariances
steering matrix
unknown reflectivity profile
a(r1,3)
a(r2,3)
a(r3,3)
a(r4,3)
.
a(rN,3)
N
h
h : number of discretization
reflectivity profile
   The task of TomoSAR is to reconstruct the reflectivity profile which is framed as the inversion of the linear system:

## Slide 30: Constraints: baseline distribution, ambiguities or replicas…
ambiguity
displacement
min baseline spacing
Ambiguity displacement
Baseline spacing
↔
small enough so that the ambiguity displacement is large enough to avoid mixing of real & replicas
Height Resolution
Baseline aperture
↔
max. distance between passes
total height of the volume in cross range
large enough for high resolution
resolution
cell
reference surface s=0
hv
va
replicas
Acr
    due to practical constraints, the quality of the tomographic imaging degrades in terms of: resolution, height ambiguities, side lobes, etc…
Ambiguity occurs in the same slant-range as the real target with displacement in the cross-range by:

## Slide 31: Factors to consider for the inversion
  The inversion must be implemented considering certain factors including:
  the distribution of the baselines
  If they are uniformly distributed, the inversion can be done with discrete Fourier Transform, however, in practice it is usually not possible to achieve constant baseline between all the tracks in air- and space-borne acquisitions
  the separation of the maximum baseline (tomographic aperture)
  The tomographic aperture defines the resolution in elevation (larger the separation, finer the resolution), due to practical constraints, such as small orbital tube of modern SAR satellites, leading to small apertures, resolution is usually degraded
  number of tracks
    limited number of tracks often results in strong undersampling leading to increased side lobes
-- Varieties of inversion techniques are presented in the SAR literature dealing with such constraints --

## Slide 32: Inversion algorithms (spectral estimators)
Capon Beam Forming (Adaptive Beamforming - ABF) with respect to FBF, Capon can not preserve radiometric calibration, however it does not require regular distribution of baselines and can reject sidelobes efficiently.
[Capon, 2003], [Gini, 2002], [Lombardini, 2003], [Nannini, 2012]
Multiple Signal Non-linear Parametric (MUSIC) are made before the application, for instance, the number of scattering mechanisms needs to be set a priori.
[Schmitt, 1986], [Gini, 2002], [Lombardini, 2013], [Li, 2016]
Compressive Sensing (CS) methods have finer resolution capabilities at elevation. The disadvantage of CS is the complexity and the high computational cost.
[Budillon, 2003], Zhu, 2011], [Aguilera, 2011], [Aguilera, 2013], [Reigber, 2000], [Reigber, 2015]
Fourier Beam Forming (FBF) is Fourier transform of the data vector estimating the backscatterer power. It is coherent and energy preserving however has limited vertical resolution and prone to ambiguities if the number of tracks is low and the baselines are irregularly distributed which is usually the case for airborne and spaceborne systems.
[Capon, 2003], [Gini, 2002], [Lombardini, 2003], [Nannini, 2012]
(tutorial)
  2 main families of inversion methods
  Parametric methods
  in order to transform the underdetermined problem into a determined one, a priori assumptions are made. The differences between the methods essentially rely on the type of assumptions
  (MUSIC, Coherence Tomography, COMET, SKP,..)
  Non-parametric methods
  the differences between methods rely on how they deal with the problem of choosing a solution among the set of possible ones (the solution is not unique due to underdetermined character).
  (Fourier Beamforming, Capon BF, Compressive Sensing,..)
Polarimetric Coherence Tomography (PCT) employs variation of the interferometric coherence with polarization. The inversion can be linearized by using a priori knowledge, volume depth and topographic phase.
[Cloude, 2006], [Pardini, 2012]

## Slide 33: Inversion algorithms - examples
Capon Beamforming – 9 tracks
MUSIC algorithm – 9 tracks
Fourier beamforming - 35 tracks
Capon Beamforming - 6 tracks
Compressive Sensing – 6 tracks
Examples of tomogram in a forest scene simulated by PolSARproSim [Tello et al. 2016].
Examples of tomogram in an agricultural scene [Joerg et al. 2015].
Identified local maxima that are not present in Capon
Peaks wrongly introduced by Compressive Sensing

## Slide 34
Advanced Techniques

## Slide 35: Polarimetric SAR Tomography
Lower image: Schematic representation of the imaged area
It is also possible to combine polarization and tomography so that different scattering contributions can be separated depending on the elevation.
Upper image: tomographic azimuth slice with Polarimetric color composite using Pauli basis
Odd bounce = HH + VV
Even bounce = HH – VV
Volume scattering = 2*HV
[Reigber & Moreira 2012]
L-band E-SAR data with 13 tracks, Oberpfaffanhofen, Germany

## Slide 36: Polarimetric SAR Tomography
An example for a polarimetric tomographic profile (corresponding to the yellow line on the SAR image) over forested area [Moreira et al. 2013]
The color coding corresponds to the elements of the Pauli vector
Blue: surface scattering (HH +VV)
Red: dihedral ground trunk interaction (HH-VV)
Green: volume scattering (2HV)
The tomographic stack contains:
21 L-band E-SAR images with an average baseline of 20 m.
Azimuth (m)
slant range (m)
1500
0
600
0
SAR image
Height (m)
0
20
Azimuth (m)
0
1500
Polarimetric tomographic profile

## Slide 37: Differential SAR Tomography : 4D & 5D imaging
Differential SAR Tomography is utilized for monitoring the targets showing displacement. It allows estimating the scatterer distribution:
for displacements: in the elevation – velocity plane
(4D imaging, 3 space + 1 velocity)
for thermal dilation: in the elevation – velocity – thermal plane
(5D imaging, 3 space + 1 velocity + thermal)
SAR Tomography + Differential SAR Interferometry  Differential SAR Tomography
Rn =
Differential TomoSAR signal model (4D):
N number of tracks acquired at different time t1…tN,
the target is located at elevation s,
to be characterized by deformation d(s,tN)
4D imaging: mean velocity[cm/year]
3D imaging: estimated topography [m]
[Reale et al. 2013]
5D imaging: thermal coefficient [cm/K]

## Slide 38
Examples and Case Studies

## Slide 39
SAR Tomography at longer wavelength (L-, P-band), offering 3D imaging capabilities and being sensitive to contributions from the vegetation layer and from the ground below, is precious in remote sensing of forested areas [Tello et al., 2015] , [Tebaldini et al., 2012]
Forest Imaging

## Slide 40: Forest Imaging: Forest Biomass and Height with SAR Tomography [Minh et al., 2016]
study area: tropical forest in Paracou & Nouragues, French Guayana
dataset: Full polarimetric, P-band ONERA data acquired in the frame of the ESA campaign TropiSAR 2009, spanning 5 uniform baselines with 15 meters.
The analysis show that the proposed TomoSAR – Biomass retrieval method is accurate even in hilly and high-biomass forest areas.
A tomographic profile at the Nouragures forest for the HV channel, white line denotes the LIDAR height measurements
Comparison between LiDAR and tomography retrieval of forest top height in both sites.
The study explores the potentials of TomoSAR to retrieve Biomass and canopy height in a tropical forest.

## Slide 41: Forest Imaging: Forest Biomass with SAR Tomography [Dinh et al., 2012]
Tomographic reconstruction of P-band along the azimuth slice of in HH, HV and VV polarizations at AA’ in the left image.
circles indicates the in-situ forest biomass measurements
AA’ line indicate the position of the tomographic slices
Two panels below show tomographic layers at:
  ground level (h=0m)
  vegetation layer (h=30m)
The aim of the study is to demonstrate the use of tomographic information to retrieve tropical forest.
It was found that reflectivity at 30m ± 10m above the ground provides the best sensitivity with forest biomass in all polarizations, for biomass ranging from 250 to 450 tons/ha.
study area: tropical forest in Paracou, French Guayana
dataset: P-band ONERA data acquired in the frame of the ESA campaign TropiSAR 2009.

## Slide 42: Forest Imaging: Forest Structure with SAR Tomography [Tello et al., 2015]
(a)-(b) Pauli representation of the tomogram with Capon and with the Compressive Sensing.
(c)-(f) Examples of inventory plots (50x50 m) with different structures, as represented
with field, LIDAR and TomoSAR data.
The study explores the link between forest structure and the 3D spatial distribution of the peaks in the reflectivity profiles at L-band, proposing measures for forest structure estimation from tomographic SAR.
The comparison of inventory plots, LIDAR and TomoSAR results indicate that the horizontal and vertical variability of the tree distribution is reflected in the tomographic profiles, essentially through the 3D spatial distribution of peaks in the reflectivity.
The tomographic profile from Compressive Sensing show better resolution and lower side lobes with respect to Capon beamforming.
study area: temperate forest In Traunstein, Germany
dataset: full polarimetric, L-band E-SAR system of DLR, spanning 5 non-uniform baselines with 5-25 meters

## Slide 43
Modern spaceborne SAR systems like TerraSAR-X, TanDEM-X, and COSMO-Skymed provide very high resolution data enabling mapping of urban infrastructure with SAR Tomography. [Zhu & Bamler, 2014]
The capabilities of SAR tomography with high resolution SAR data includes reconstruction of single buildings, the estimation of deformation mean velocity, as well as detection of thermal dilation.
Urban Imaging

## Slide 44: Urban Imaging: SAR Tomography for imaging urban areas [Zhu & Bamler, 2014]
The study presents the concept of SL1MMER algorithm based on the inversion with Compressive Sensing for multi-dimensional imaging of Urban areas.
-30
linear deformation velocity [mm/yr]
0
TomoSAR deformation estimates around Las Vegas Convention Center
TomoSAR point cloud from 94 ascending & 79 descending TerraSAR-X images of Berlin, Germany
Point cloud of Bellagio Hotel, Las Vegas generated by 25 TerraSAR-X images visualized in Google Earth (DLR)
Reconstructed building facades of
Bellagio Hotel
https://www.youtube.com/embed/BrpDRdhBhcQ?autoplay=1
Also see the video: Tomographic City Tour of Berlin from Space

## Slide 45: Urban Imaging: 4D & 5D imaging [Fornaro et al., 2012]
study area: city of Las Vegas, USA
dataset: 25 TerraSAR-X images in high resolution spotlight mode
residual topography
-50 m
100 m
The study investigates the application of SAR tomography to very high resolution TerraSAR-X data in order to demonstrate the potentials for monitoring of transportation infrastructures showing deformation and thermal dilation.
TomoSAR height estimation
deformation mean
velocity
thermal dilation
coefficient

## Slide 46: Urban Imaging: 4D & 5D imaging [Reale et al., 2013]
Estimated thermal coefficient [mm/K]
4D imaging: mean velocity[cm/year]
5D imaging: thermal coefficient [cm/K]
3D imaging: estimated topography [m]
study area: city of Las Vegas, USA
dataset: 25 TerraSAR-X images in high resolution spotlight mode
The study addresses the extension of tomographic based approaches to the monitoring of structure thermal dilation.
Aspects related to,
detection of the scatterers
estimation of the thermal coefficient beside the topography and deformation mean velocity
are investigated.

## Slide 47
SAR tomography offers an opportunity to observe the internal structure of glaciers and polar ice sheets, to expand the knowledge and understanding of the processes related to ice formation and melting, the water movement through a glacier, and for assessing the response of the ice masses to climate forcing [Tebaldini et al., 2016].
Ice/Snow Imaging

## Slide 48: Ice & Snow Imaging : Estimation of Ice penetration depth [Banda et al., 2014]
study area: ablation zone of South-West Greenland
dataset: Airborne P-band POLARIS data in HH polarization
The study addresses quantitative analysis of the penetration depth of P-band SAR signal into ice subsurface.
ground range slice
The white lines denote the upper and lower ice boundaries as estimated by the MUSIC algorithm [Banda et al. 2014]
tomographic section obtained by Capon estimator at 40 m below the vertical phase center.
azimuth slice

## Slide 49: Ice & Snow Imaging : Imaging internal structure of glacier [Tebaldini et al., 2016]
study area: Mittelbergferner glacier, Austrian Alps
dataset: Airborne L-band data in HH and HV polarization
The study reports the analysis of L-band airborne TomoSAR application for imaging the internal structure of a glacier.
Various sub-surface features including firn bodies, crevasses, layer transition, bedrock reflection down to 50 m below the ice surface, observed in GPR (Ground Penetrating Radar) are also captured in TomoSAR slices.
Vertical stripes are observed ranging from the ice surface to about 20 m in depth with increased amplitudes, which are typical features indicating crevasses
The bedrock underneath homogeneous ice appears as very sharp reflection due to strong gradients in dielectric properties at the transition ice–rock.
Ground Ranging Radar
Ground Ranging Radar

## Slide 50
The scattering mechanisms in agricultural vegetation are rather complex due to the different species, orientation of the vegetation volume and very fast changes in the structure of the vegetation over the phenological cycle.
SAR tomography can be utilized to resolve the scattering processes in the vertical direction, to separate the ground and volume backscattering and to interpret the effect of physical changes of species, phenological state, etc [Joerg et al., 2015].
Agriculture Imaging

## Slide 51: Agriculture Imaging: Polarimetric Tomography for Phenological Changes of Agricultural Crops [Joerg et al., 2017]
0
1
Capon Slices
multi-look cell 7.5⨯7.5m
(X-/C-band: 220 looks,
L-band: 100 looks)
0m
0m
0m
4m
4m
4m
X-BAND
ρz=0.5m
9 tracks
C-BAND
ρz=0.8m
9 tracks
L-BAND
ρz=1.2m
8 tracks
JULY 3
HH
HH
HH
VV
VV
VV
Corn
Wheat
Barley
Corn
Corn
Wheat
Barley
Corn
450m
450m
The study investigates the impact of changes in agriculturally vegetated areas on the scattering signatures at different frequencies.
The main challenges of monitoring of agricultural vegetation include:
  high resolution and high accuracy required
  many influencing parameters, e.g. crop height, soil moisture & roughness, vegetation water content, orientation characteristics etc..
  complex scattering scenario
ρz : vertical
resolution
study area:
Wallerfing, Germany
dataset:
Airborne X, C-,L-band
F-SAR data in
Quad polarization
Corn
Wheat
Barley
July 03
Crop Height [m] at data acquisition

## Slide 52: Agriculture Imaging: Polarimetric Tomography for Phenological Changes of Agricultural Crops [Joerg et al., 2017]
0
1
Capon Slices
multi-look cell 7.5⨯7.5m
(X-/C-band: 220 looks,
L-band: 100 looks)
0m
0m
0m
4m
4m
4m
X-BAND
ρz=0.5m
9 tracks
C-BAND
ρz=0.8m
9 tracks
L-BAND
ρz=1.2m
8 tracks
JULY 24
HH
HH
HH
VV
VV
VV
Corn
Wheat
Barley
Corn
Corn
Wheat
Barley
Corn
450m
450m
study area:
Wallerfing, Germany
dataset:
Airborne X, C-,L-band
F-SAR data in
Quad polarization
ρz : vertical
resolution
Corn
Wheat
Barley
July 03
July 24
Crop Height [m] at data acquisitions
The study reports that even though the Rayleigh resolution in height is in the range of the vegetation heights,
changes in the scattering characteristics could be detected
the differences between the species and the stages of the phenological cycle, growth & penetration capabilities, could be observed.

## Slide 53: Agriculture Imaging: Polarimetric Tomography for Phenological Changes of Agricultural Crops [Joerg et al., 2017]
Interpretations:
L-band:
  In contrast to higher frequencies, L-band is not as sensitive to low vegetation and the vertical profiles are in general more ground dominated.
  The vertical resolution is lower than at the higher frequencies which makes it more difficult to distinguish between contributions at different heights, particularly for low plant height.
  Additionally in the corn, on July 24th, VV has an increased sensitivity to the vegetation compared to HH where ground contribution is more dominant.
Corn
Wheat
Barley
X- and C-band:
  Similar characteristics are observed at X- and C-band while the profiles at X-band show more volume contribution.
  In the corn, the growth and the morphological change of the plants are observed.
  In the wheat, the dryout can be observed by the main peak of the vertical profiles moving from the top of the plant closer to the ground from one date to the other.
  The extent of the vertical profiles in both dates are, however, smaller than the actual plant height indicating that also high frequencies penetrate into the vegetation.

## Slide 54
References & Further Reading

## Slide 55: References & Further Reading
Aguilera (a), E., Nannini, M, and Reigber, A. (2013), “A Data-Adaptive Compressed Sensing Approach to Polarimetric SAR Tomography of Forested Areas”. IEEE Geoscience and Remote Sensing Letters, Vol. 10, No. 3, pp. 543–547.
Aguilera (b), E., Nannini, M, and Reigber, A. (2013), “Wavelet-based compressed sensing for SAR tomography of forested areas”. IEEE Trans. Geosci. Remote Sens., Vol. 51, No. 12, pp. 5283–5295.
Budillon, A., Evangelista, A. and Schirinzi, G. (2011), “Three-dimensional SAR focusing from multipass signals using compressive sampling,” IEEE Trans. Geosci. Remote Sens., vol. 49, no. 1, pp. 488–499.
Capon, J. (2003). “High resolution frequency wavenumber spectrum analysis”. Proceedings of the IEEE, Vol. 150, No. 3, pp. 125-134.
Cloude, S. (2006), “Polarization Coherence Tomography,” Radio Science, vol. 41, RS4017.
Danisor, C., Fornaro, G., & Datcu, M. (2016). “Inversion Algorithms and PS Detection in SAR Tomography, Case Study of Bucharest City”. Telfor Journal, 8, 1.
Ferro-Famil, L. (2015). PolSARpro 2015 Lectures, ESA-ESRIN, Frascati(Rome), Italy, 19-23 January 2045.
Fornaro, G. (2014). ”Tomographic SAR”. NATO SET-191 Lecture Series, Bucharest, 10-11 November.
Fornaro, G. & Pascazio, V., (2013). “SAR Interferometry and Tomography: Theory and Applications”, Academic Press Library in Signal Processing vol. 2, Elsevier Ltd.
Gini, F., Lombardini, F. and Montanari, M. (2002), “Layover solution in multibaseline SAR interferometry,” IEEE Transactions on Aerospace and Electronic Systems, vol. 38, pp. 1344–1356.
Li, X., Liang, L., Guo, H. and Huang, Y. (2016). “Compressive Sensing for Multibaseline Polarimetric SAR Tomography of Forested Areas”, IEEE Transactions on Geoscience and Remote Sensing, Vol. 54, No. 1, pp. 153-166.
Lombardini, F. and Reigber, A., (2003) “Adaptive spectral estimation for multibaseline SAR tomography with airborne L-band data,” Proceedings of International Geoscience and Remote Sensing Symposium, vol. 3, pp. 2014–2016.
Lombardini, F., Cai, F. and Pasculli, D., (2013), “Spaceborne 3-D SAR Tomography for analyzing garbled urban scenarios: Single-look superresolution advances and experiments,” IEEE Journal of Selected Topics in Applied Earth Observations and Remote Sensing, vol. 6, no. 2, pp. 960–968.
TomoSAR General

## Slide 56: References & Further Reading
Moreira, A., Prats-Iraola, P., Younis, M., Krieger, G., Hajnsek, I., & Papathanassiou, K. P. (2013). “A Tutorial on Synthetic Aperture Radar”. IEEE Geoscience and Remote Sensing Magazine, 1, pp. 6-43.
Nannini, M. , Scheiber, R. , Horn, R. and Moreira, A., (2012), “First 3-D reconstructions of targets hidden beneath foliage by means of Polarimetric SAR Tomography,” Geoscience and Remote Sensing Letters, IEEE, vol. 9, no. 1, pp. 60–64.
Papathanassiou, K. (2013). 4th Advanced Training Course in Land Remote Sensing Slides, 01 - 05 July 2013, Harokopio University, Athens, Greece
Pardini, M., Torano-Caicoya, A., Kugler, F., Lee, S. K., Hajnsek, I. and K. Papathanassiou, (2012), “On the estimation of forest vertical structure from multibaseline polarimetric SAR data,” Proceedings of International Geoscience and Remote Sensing Symposium, pp. 3443–3446.
Reigber, A., & Moreira, A. (2000). “First Demonstration of Airborne SAR Tomography using Multibaseline L-band Data”. IEEE Transactions On Geoscience And Remote Sensing, 38, no. 5., pp. 2142-2152
Reigber, A., Nannini, M., Martinez del Hoyo, A., (2015), “A Comparative Study of Tomographic SAR Focusing Methods”, Proceedings on the 12th European Radar Conference, pp. 29-32
Richards, J. (2009). “Remote Sensing with Imaging Radar”. Springer, pp 209-217.
Schmidt, R. (1986), “Multiple emitter location and signal parameter estimation”. IEEE Transactions on Antennas and Propagation, Vol. 34, No. 3, pp. 279-280.
Tebaldini, S. (2012). “Remote Sensing of Biomass - Principles, chapter: Forest Structure Retrieval from Multi-Baseline SARs”. Temilola Fatoyinbo, InTech, pp. 28-58
Zhu, X. and Bamler, R., (2010), “Tomographic SAR Inversion by L1-norm Regularization – The Compressive Sensing Approach”, IEEE Trans. on Geoscience and Remote Sensing, Vol. 48, No. 10, pp. 3839 – 3846
TomoSAR General

## Slide 57: References & Further Reading
Forest Imaging
Minh, D.H.T, Toan, T. L., Rocca, F., Tebaldini, S., Villard, L., Rejou-Mechain, M., Phillips, O. L. , Feldpausch, T. R., Dubois-Fernandez, P., Scipal, K. Chave, J. (2016). “SAR tomography for the retrieval of forest biomass and height: Cross-validation at two tropical forest sites in French Guiana”. Remote Sensing of Environment, 175, 138-147.
Pardini, M., Cantini, A., Lombardini, F., & Papathanassiou, K. P. (2014). 3-D Structure of Forest: First Analysis of Tomogram Changes due to Weather and Seasonal Effects at L-band. Proc. of EUSAR, June 2014, Berlin.
Schmitt, M., Shahzad, M., & Zhu, X. (2015). „Reconstruction of individual trees from multi-aspect TomoSAR data”. Remote Sensing of Environment, 165, 175-185.
Tebaldini, S., & Rocca, F. (2012). “Multibaseline Polarimetric SAR Tomography of a Boreal Forest at P- and L-Bands”. IEEE Transactions on Geoscience and Remote Sensing, 50, No.1.
Tello, M., Cazcarra-Bes, V., Pardini, M., & Papathanassiou, K. P. (2015). “Structural Classification of Forest By Means of L-band Tomographic SAR”. IGARSS2015, Milan, Italy, 26-31 July.
Tello, M., Cazcarra-Bes, V., Pardini, M., & Papathanassiou, K. P. (2016). “Assessment of forest structure estimation by means of SAR Tomography potentials and limitations”. IGARSS2016, Beijing, China, 10-15 July.
Banda, F., Tebaldini, S., & Rocca. (2014). “Ice Penetration Depth Estimation from Super-Resolution SAR Tomography”. Proceedings of the 11th European Radar Conference, Rome, Italy, 8-10 October, 2014.
Tebaldini, S., Nagler, T., Rott, H., & Heilig, A. (2016). “Imaging the Internal Structure of an Alpine Glaicer via L-band Airborne SAR Tomography”. IEEE Transactions on Geoscience and Remote Sensing, 54, No. 12.
Ice/Snow Imaging

## Slide 58: References & Further Reading
Urban Imaging
Fornaro, G., Pauciullo, A., Reale, D., & Verde, S. (2014). Multilook SAR Tomography for 3-D Reconstruction and Monitoring of Single Structures Applied to COSMO-SKYMED Data. IEEE Journal Of Selected Topics In Applied Earth Observations And Remote Sensing, 7, 4.
Fornaro, G., Pauciullo, A., Reale, D., Zhu, X., & Bamler, R. (2012). SAR Tomography: “An Advanced Tool For 4D Spaceborne Radar Scanning with Application to Imaging and Monitoring Of Cities And Single Buildings”. IEEE Geoscience and Remote Sensing Society Newsletter.
Fornaro, G., Reale, D., and Verde, S. (2012), “Potential of SAR for Monitoring Transportation Infrastructures: an Analysis with the Multi-Dimensional Imaging Technique,” J. Geophys. Eng. 9 S1
Fornaro, G., & Serafino, F. (2006). “Imaging of Single and Double Scatterers in Urban Areas via SAR Tomography”. IEEE Transactions on Geoscience and Remote Sensing, 44, 12.
Reale, D., & Fornaro, G. (2014). “SAR Tomography for 3D Reconstruction and Monitoring”. Encyclopedia of Earthquake Engineering, Springer, pp. 1-16.
Reale, D., Fornaro, G. and Pauciullo, A. (2013). “Extension of 4-D SAR Imaging to the Monitoring of Thermally Dilating Scatterers” . IEEE Transactions on Geoscience and Remote Sensing, 51, 10.
Reale, D., Fornaro, G., A.Pauciullo, X.Zhu, & Bamler, R. (2011). “Tomographic Imaging and Monitoring of Buildings With Very High Resolution SAR Data”. IEEE Geoscience and Remote Sensing Letters, 8, 4.
Zhu, X. X., & Bamler, R. (2014). Superresolving SAR Tomography for Multidimensional Imaging of Urban Areas: Compressive sensing-based TomoSAR inversion. IEEE Signal Processing Magazine, 31, 51-58.
Zhu, X. X., & Bamler, R. (2010). Very High Resolution Spaceborne SAR Tomography in Urban Environment. IEEE Transactions on Geoscience and Remote Sensing, 48, 12.
Joerg, H., Pardini, M., Hajnsek, I., & Papathanassiou, K. P. (2017). “Fully Polarimetric Tomographic Time Series for Monitoring Phenological Changes of Agricultural Crops at Different Frequencies”. Proceedings of ESA POLinSAR 2017, Frascati (Rome), Italy, 23 - 27 January.
Joerg, H., Pardini, M., Hajnsek, I., & Papathanassiou, K. P. (2015). “Application Of Polarimetric SAR Tomography On Agricultural Vegetation For Scattering Characterisation”. Proceedings of ESA POLinSAR 2015, Frascati (Rome), Italy, 26 - 30 January.
Agriculture Imaging

## Slide 59
SAR-EDU
SAR Remote Sensing Education Initiative
https://eo-college.org
F-SAR data for the SAR Tomography Tutorial is provided by DLR (German Aerospace Center)